## Slide 1: Update on Methane Regulations Affecting Landfills
Pat Sullivan
Senior Vice President
SCS Engineers
Nov. 10, 2015

## Slide 2: Agenda
Background on Rulemaking
Schedule and Implementation
Applicability
Summary of Key Issues
Requests for Comment
Impacts on LFGTE

## Slide 3: Federal NSPS/EG Proposals
August 27, 2015--published in Federal Register
Expect NSPS and EG to have same requirements
  Supplemental NSPS Subpart XXX (40 CFR Part 60)
    Applies to New, Modified or Reconstructed landfills after July 17, 2014
    Industry comments previously provided September 2014
  Proposed EG Subpart Cf (40 CFR Part 60)
    Replacing Subpart WWW & Cc
    Applies to existing landfills accepted waste after 11-8-1987 and began construction, reconstruction or modification before July 17, 2014

## Slide 4: Schedule and Implementation
60-day comment period ended October 26, 2015
  Solid waste industry comments submitted
Anticipate final rule action July 2016
NSPS XXX when issued will be final and effective
For EG Cf, States have 9 months to submit Plans
  EPA then has 4 months to review and approve
Waiting on EPA to propose Federal Plan

## Slide 5: Thresholds for Installing Methane Controls
Design capacity threshold
  Remain the same—2.5 million Mg and m3
NMOC emission threshold
  Reduced from 50 Mg/year down to 34 Mg/year
  Closed landfills remain at 50 Mg/year (Subcategory)
Impact:
  Results in certain landfills triggering requirement to install/operate a GCCS earlier or where they would not have otherwise
  Key element of rules to create additional methane reductions
  More potential sites for energy recovery

## Slide 6: Wellhead Standards
Removal of Oxygen/Nitrogen & Temperature
  Monthly monitoring still required
  Fluctuations/variations no longer require corrective action or reportable; must maintain records on-site
  Maintain negative pressure as currently required
Impact:
  Eliminates HOVs and timeline requests/approvals
    Reduces cost for recordkeeping and reporting
  Reduces liability for wellhead exceedances & gives greater operational flexibility of the wellfield
  Should improve gas recovery and reduce emissions

## Slide 7: LFG Treatment
Defining Treatment System
  System that filters, de-waters and compresses landfill gas to levels determined by the landfill based on the beneficial end use of the gas
    Retaining alternative definition of LFG treatment based on specific numerical values for filtration and de-watering
  Develop site-specific treatment monitoring plan to:
    Identify monitoring parameters
    Conduct monitoring
    Keep records
    Demonstrate that Plan shows compliance with filtration, de-watering, and compression system criteria

## Slide 8: LFG Treatment (cont.)
Clarification that treated LFG is not just limited to fuel combusted in stationary combustion devices but is also allowed in other beneficial uses or devices.
Impact:
  Additional beneficial use projects will qualify to use the treatment exclusion
  No stack testing, control device monitoring, or SSM criteria for beneficial use projects

## Slide 9: LFG Treatment (cont.)
Impact:
  Allows flexibility to use treatment to demonstrate compliance.
  EPA still evaluating numerical values as an alternative which could have negative impact if those requirements are in the final rule.
  Monitoring Plan must be approved by the state/local agency
    Opportunity for states to define limits/monitoring?

## Slide 10: SSM Issues
The Landfill NESHAPs was promulgated on January 16, 2003 (68 FR 2227, 40 CFR Part 63 Subpart AAAA).
All NSPS and EG landfills subject to the GCCS requirements must comply with the landfill NESHAPs
  Not changing with NSPS/ES proposals
  Prepare, follow, and maintain a startup, shutdown, and malfunction (SSM) plan for the GCCS.

## Slide 11: SSM Issues (cont.)
Landfill NESHAPs rule does not have any emission limits
  Our only limits appear in the NSPS/EG rules
As a result of NESHAPs lawsuit, compliance exemptions during SSM events were disallowed by EPA
However, our compliance exemption is contained within our NSPS rule (WWW) ---still valid
  40 CFR 60.755[e]. “The provisions of this subpart apply at all times, except during periods of SSM, provided the during of the SSM shall not exceed 5 days for collection systems and 1 hour for control devices.”
In draft NSPS (XXX) and EG (Cf) rules, EPA proposed to take away our exemption language---standards apply at all times including SSM

## Slide 12: SSM Issues (cont.)
What will happen if EPA moves forward on the proposed change?
  All SSM events could be rule deviations; potential for NOVs, fines, and excess emission fees
  We would be required to calculate excess NMOC emissions during periods of SSM
  In general, energy projects create more potential SSM events, so may increase compliance liability
    Treatment exemption even more important
  Need allowances for non-SSM downtime events for GCCS and portions thereof

## Slide 13: Request for Comments
EPA seeking comments on the following topics:
  Organics Diversion
  Requiring energy recovery
Impact:
  EPA will have the ability to add additional provisions into the final version of the rules based on the information submitted as a part of these requests
  Each would have its own impact on beneficial use of LFG

## Slide 14: Impacts on LFGTE
Organics Diversion
  Reduces methane generation and amount of energy available
Requiring Energy Recovery
  More potential projects but no regard for economic viability
Treatment Exemption
  Simple definition with limited monitoring will reduce costs and limit compliance issues for new and existing projects

## Slide 15: Impacts on LFGTE (cont.)
Lowering NMOC Threshold
  More methane recovery but generally smaller sites where economics not as conducive
Removal of Wellhead Criteria
  More flexible GCCS operation beneficial to methane recovery
Loss of SSM Exemption
  Presents more potential compliance liability for LFGTE equipment and GCCS